## Slide 1: Computer systems fundamentals ( 4COSC004w )
Lecture: Week 2

## Slide 2: Previous week:
Introduction to the module
  Structure
  Administration
Positional Number Systems
  Denary
  Binary

## Slide 3: Tutorials
See YOUR personalised timetable to find out time & tutor
Online exercises on Blackboard - Live now
  Apps to help
Tutor available to assist
Will cover all topics from lectures
Feedback after each attempt
Re-attempt each exercise until you achieve full marks

## Slide 4: Hexadecimal Base 16
Positive Integers

## Slide 5: By the end of this lecture, you will:
Be able to convert Hexadecimal Positive Integers to their Binary values
Be able to convert Binary Positive Integers to their Hexadecimal values
Be able to convert Hexadecimal Positive Integers to their Denary values

## Slide 6: Hexadecimal
Base-16
Each digit can be a value 0-F
  One of 16 different values
Denary | Hexadecimal
0 | 0
1 | 1
2 | 2
3 | 3
4 | 4
5 | 5
6 | 6
7 | 7
8 | 8
9 | 9
10 | A
11 | B
12 | C
13 | D
14 | E
15 | F

## Slide 7: Why Hexadecimal?
Denary works well for us humans
Binary works for digital computers
  00101011
  0100101000101011
Hexadecimal is convenient way to represent Binary values:
  Base-16
  One Hexadecimal digit maps to a 4-Bit Binary Nibble
  Each 4-Bit Binary Nibble maps to a Hexadecimal digit

## Slide 8: Hexadecimal Table
Denary | Binary |  |  |  | Hexadecimal
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
2 | 0 | 0 | 1 | 0 | 2
3 | 0 | 0 | 1 | 1 | 3
4 | 0 | 1 | 0 | 0 | 4
5 | 0 | 1 | 0 | 1 | 5
6 | 0 | 1 | 1 | 0 | 6
7 | 0 | 1 | 1 | 1 | 7
8 | 1 | 0 | 0 | 0 | 8
9 | 1 | 0 | 0 | 1 | 9
10 | 1 | 0 | 1 | 0 | A
11 | 1 | 0 | 1 | 1 | B
12 | 1 | 1 | 0 | 0 | C
13 | 1 | 1 | 0 | 1 | D
14 | 1 | 1 | 1 | 0 | E
15 | 1 | 1 | 1 | 1 | F

## Slide 9: Binary: Bit weightings
Denary | Binary |  |  | 
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
23 | 22 | 21 | 20
8 | 4 | 2 | 1

## Slide 10: Binary: Bit weightings
Denary | Binary |  |  | 
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 1 | 1
4 | 0 | 1 | 0 | 0
5 | 0 | 1 | 0 | 1
6 | 0 | 1 | 1 | 0
7 | 0 | 1 | 1 | 1
8 | 1 | 0 | 0 | 0
9 | 1 | 0 | 0 | 1
10 | 1 | 0 | 1 | 0
11 | 1 | 0 | 1 | 1
12 | 1 | 1 | 0 | 0
13 | 1 | 1 | 0 | 1
14 | 1 | 1 | 1 | 0
15 | 1 | 1 | 1 | 1
Denary | Binary |  |  |  | Hexadecimal
0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
2 | 0 | 0 | 1 | 0 | 2
3 | 0 | 0 | 1 | 1 | 3
4 | 0 | 1 | 0 | 0 | 4
5 | 0 | 1 | 0 | 1 | 5
6 | 0 | 1 | 1 | 0 | 6
7 | 0 | 1 | 1 | 1 | 7
8 | 1 | 0 | 0 | 0 | 8
9 | 1 | 0 | 0 | 1 | 9
10 | 1 | 0 | 1 | 0 | A
11 | 1 | 0 | 1 | 1 | B
12 | 1 | 1 | 0 | 0 | C
13 | 1 | 1 | 0 | 1 | D
14 | 1 | 1 | 1 | 0 | E
15 | 1 | 1 | 1 | 1 | F
23 | 22 | 21 | 20
8 | 4 | 2 | 1

## Slide 11: Hexadecimal table
Binary |  |  |  | Hexadecimal
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
1 | 0 | 1 | 0 | A
1 | 0 | 1 | 1 | B
1 | 1 | 0 | 0 | C
1 | 1 | 0 | 1 | D
1 | 1 | 1 | 0 | E
1 | 1 | 1 | 1 | F

## Slide 12: Try it for yourself
Generate the Hexadecimal Nibble (4-bit) Table with its corresponding columns for Binary and Hexadecimal values

## Slide 13: Hexadecimal table
Binary |  |  |  | Hexadecimal
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
1 | 0 | 1 | 0 | A
1 | 0 | 1 | 1 | B
1 | 1 | 0 | 0 | C
1 | 1 | 0 | 1 | D
1 | 1 | 1 | 0 | E
1 | 1 | 1 | 1 | F

## Slide 14: Converting from Hexadecimal to Binary
Binary |  |  |  | Hexadecimal
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
1 | 0 | 1 | 0 | A
1 | 0 | 1 | 1 | B
1 | 1 | 0 | 0 | C
1 | 1 | 0 | 1 | D
1 | 1 | 1 | 0 | E
1 | 1 | 1 | 1 | F
2 |  |  |  | A |  |  |  | B |  |  |  | 3 |  |  | 
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1

## Slide 15: Converting from Binary to Hexadecimal
Binary |  |  |  | Hexadecimal
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 2
0 | 0 | 1 | 1 | 3
0 | 1 | 0 | 0 | 4
0 | 1 | 0 | 1 | 5
0 | 1 | 1 | 0 | 6
0 | 1 | 1 | 1 | 7
1 | 0 | 0 | 0 | 8
1 | 0 | 0 | 1 | 9
1 | 0 | 1 | 0 | A
1 | 0 | 1 | 1 | B
1 | 1 | 0 | 0 | C
1 | 1 | 0 | 1 | D
1 | 1 | 1 | 0 | E
1 | 1 | 1 | 1 | F
0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 1 | 1
2 |  |  |  | A |  |  |  | B |  |  |  | 3 |  |  | 

## Slide 16: Try it for yourself
Convert a long (no less than sixteen bits long) binary number to Hexadecimal
Convert the Hexadecimal value you found back to Binary

## Slide 17: Number System Triangle
Denary
Binary
Hexadecimal

## Slide 18: Converting from Hexadecimal to Denary
Base 16
Weighting of each position are successive powers of 16
 |  | 6 | 

## Slide 19: Multiples of powers of 16
16 table | 
1 | 16
2 | 32
3 | 48
4 | 64
5 | 80
6 | 96
7 | 112
8 | 128
9 | 144
10 | 160
11 | 176
12 | 192
13 | 208
14 | 224
15 | 240
256 table | 
1 | 256
2 | 512
3 | 768
4 | 1024
5 | 1280
6 | 1536
7 | 1792
8 | 2048
9 | 2304
10 | 2560
11 | 2816
12 | 3072
13 | 3328
14 | 3584
15 | 3840
4096 table | 
1 | 4096
2 | 8192
3 | 12288
4 | 16384
5 | 20480
6 | 24576
7 | 28672
8 | 32768
9 | 36864
10 | 40960
11 | 45056
12 | 49152
13 | 53248
14 | 57344
15 | 61440

## Slide 20: Number System Triangle
Denary
Binary
Hexadecimal

## Slide 21: In this lecture we have covered:
Hexadecimal:
  Converting values from Hexadecimal to Binary
  Converting values from Binary to Hexadecimal
  Converting values from Hexadecimal to Decimal

## Slide 22: Further reading:
Foundation Maths
  Chapter 14
Computer Science Illuminated
  Chapter 2

## Slide 23: Thank you
© The University of Westminster (2023)
These slides have been reviewed and amended by Adem Coskun, Izzet Kale and George Charalambous.
The right of Noam Weingarten to be identified as author of this work has been asserted by them in accordance with the Copyright, Designs and Patents Act 1988